## Slide 1
UAM Corridor
Communication–Transportation Simulation
A coupled discrete-time model of UAV traffic & communication for Urban Air Mobility corridors
Yanbing Wang (Arizona State University) · Toyota InfoTech Lab· Made with Claude Code
March 2026 · For internal research use — Toyota ITL / ASU collaboration
PROTOTYPE

## Slide 2
NAVIGATION
Contents
UAM Corridor Simulation · Toyota/TEMA 2026
01
Objective & Architecture
System overview and design goals
Slides 03–04
02
Traffic Layer
UAV model, corridor, car-following
Slides 05–07
03
Infrastructure Layer
Base stations, placement, M/M/1
Slides 08–10
04
Network Layer
Messages, RTT, handoff algorithm
Slides 11–13
05
KPI Definitions
Safety and performance metrics
Slides 14–15
06
Scenarios
4 prototype experiments and results
Slides 16–20
07
Validation & Roadmap
Limitations and next steps
Slides 21–22
08
Appendix
Equations and parameter table
Slides 23–24

## Slide 3
INTRODUCTION
Research Objective
UAM Corridor Simulation · Toyota/TEMA 2026
Quantify how UAV traffic density and human–control mode transitions stress shared 5G cellular infrastructure — and identify the parameter regimes in which that coupling becomes safety-critical.
Coupled model
Co-simulate UAM kinematics and cellular queuing in a unified discrete-time loop
HOTL / HWTL stress test
Quantify bandwidth demand spike when aircraft switch from supervisory to manual (video) mode
Shared infrastructure risk
Model terrestrial 5G users competing for the same BS capacity as aerial vehicles
Scenario stress testing
Run 4 experiments spanning normal operations through cascade infrastructure failure

## Slide 4
INTRODUCTION
Simulation Architecture
UAM Corridor Simulation · Toyota/TEMA 2026
1
Position Update
Car-following law
advances all UAMs
›
2
Mode Switching
Poisson timers
HOTL ↔ HWTL
›
3
Coverage & Handoff
Nearest-BS assignment
hysteresis check
›
4
Traffic & Queuing
M/M/1 queuing delay
RTT computation
›
5
KPI Recording
Time-series metrics
written to collector
Each step repeats in strict sequential order; no sub-stepping or parallelism.

## Slide 5
TRAFFIC LAYER
Corridor Definition
UAM Corridor Simulation · Toyota/TEMA 2026
Parameter | Symbol | Value
Corridor length | L | 80,000 m (80 km)
Cruise altitude AGL | h | 300 m
Vertical band thickness | Δh | 33 m
Number of lanes | Nℓ | 1 (baseline), 2 (high-density)
Origin hub | SF | x = 0 m
Destination hub | SJ | x = L
SF–SJ Corridor
Lane 0
SF
SJ
h = 300 m AGL
80 km →
Boundary condition: UAMs wrap around at x = L (continuous-flow).
Lateral lane position is a discrete integer label — not geometrically resolved.

## Slide 6
TRAFFIC LAYER
UAV Kinematic Model
UAM Corridor Simulation · Toyota/TEMA 2026
State vector per vehicle i:
(xᵢ, vᵢ, modeᵢ, BSᵢ)
Uniform spawn:
xᵢ(0) = L / (N+1) × i
vᵢ(0) ~ min(Uniform(v_min, v_max), (xi-1(0)- xᵢ(0))/ τ_min
Car-following law:
Leader (free-flow):
x_lead(t+Δt) = x_lead(t) + v_lead × Δt
Follower (if gap < vᵢ × τ_min):
vᵢ* = max(Δx / τ_min, 0)
xᵢ(t+Δt) = xᵢ(t) + vᵢ × Δt
Scenario | N | v_min | v_max | τ_min
Baseline | 50 | 40 m/s | 60 m/s | 5 s
High density | 150 | 35 m/s | 55 m/s | 3 s
Freq. switches | 80 | 40 m/s | 60 m/s | 5 s
Cascade failure | 60 | 40 m/s | 55 m/s | 5 s
Separation Metric
T_sep,i = (x_{i+1} - x_i) / v_i
Violation recorded when T_sep,i < τ_viol = 2.0 s
Known limitation: instantaneous speed adjustment (no inertia).
Planned replacement: IDM or eVTOL thrust/drag model.

## Slide 7
TRAFFIC LAYER
Human–Control Mode Switching
UAM Corridor Simulation · Toyota/TEMA 2026
HOTL
Human-Over-The-Loop
Automation manages flight
Human monitors only
35 kbps telemetry
HWTL
Human-Within-The-Loop
Human actively pilots
via live video feed
6 Mbps video stream
↔
~100×
bandwidth ratio
HWTL vs HOTL
Poisson Mode-Switch Model
T_switch ~ Exp(λ), λ = λ_hr / 3600 [s⁻¹]
D_HWTL ~ Exp(μ), μ = 1 / d̅ [s⁻¹]
Scenario | λ_hr | Mean HWTL duration d̅
Baseline | 0.5 / UAM / hr | 60 s
Frequent switches | 5.0 / UAM / hr | 45 s
Cascade failure | 8.0 / UAM / hr | 90 s
Also supported: zone-based triggers (hot-zones near hubs with per-step switch probability p_zone × Δt)
E[concurrent HWTL/BS] = (λ_hr/3600) × d̅ × N_BS
Cascade scenario: (8/3600) × 90 × 10 ≈ 2 concurrent HWTL per BS → ρ ≈ 63%

## Slide 8
INFRASTRUCTURE LAYER
Base Station Specifications
UAM Corridor Simulation · Toyota/TEMA 2026
Each BS abstracts a 5G NR gNB ground node with fixed bandwidth capacity and an M/M/1 uplink queue.
Parameter | Symbol | Baseline | High Density | Cascade Failure
Number of BS | M | 16 | 16 | 6
BS capacity | C | 100 Mbps | 50 Mbps | 20 Mbps
Good-coverage radius | r_good | 3,000 m | 3,000 m | 5,000 m
Degraded-coverage radius | r_deg | 6,000 m | 6,000 m | 9,000 m
Message buffer capacity | B | 500 msgs | 300 msgs | 500 msgs
BS spacing (uniform) | Δx | ≈4,706 m | ≈4,706 m | ≈11,429 m
Coverage quality: 3-tier threshold on 3D Euclidean distance
Good
d ≤ r_good
Degraded
r_good < d ≤ r_deg
None
d > r_deg (coverage gap)

## Slide 9
INFRASTRUCTURE LAYER
Infrastructure Placement
UAM Corridor Simulation · Toyota/TEMA 2026
Placement equations
x_jᴵˢ = (L / (M+1)) × j, j = 1, ..., M
y_jᴵˢ = 500 m (lateral offset from corridor)
3D UAM–BS distance
d_ij = √[ (x_jᴵˢ - x_i)² + (y_jᴵˢ)² + h² ]
UAM y-position projected to corridor centerline (y_UAM = 0)
BS–GCS backhaul: always up, RTT_bh = 10 ms
Corridor cross-section view (not to scale)
Corridor (h = 300 m AGL)
BS1
BS2
BS3
BS4
BS5
y_BS = 500 m (lateral)
Baseline: Δx ≈ 4,706 m · Cascade: Δx ≈ 11,429 m · Good coverage r = 3 km (overlap at baseline spacing)

## Slide 10
INFRASTRUCTURE LAYER
M/M/1 Queuing Model
UAM Corridor Simulation · Toyota/TEMA 2026
Traffic intensity (utilization):
ρ_j = Σ_i ∈ S_j R_i / C_j
where S_j = set of UAMs served by BS j, R_i = per-UAM bit rate, C_j = BS capacity
Mean queuing delay (M/M/1 mean sojourn):
W_j = L_min / (1 - ρ_j), ρ_j < 1
L_min = 5 ms (base processing latency, serialization + scheduling)
W_j = 2.0 s (saturated cap) if ρ_j ≥ 1
Buffer overflow check (independent of bit-rate):
if msgs_arrived > B: drop excess (B = 500 msgs)
Load level | Threshold | Behaviour
Normal | ρ < 0.60 | W grows slowly with ρ
Warning | ρ ≥ 0.60 | Queue builds; RTT rises
Critical | ρ ≥ 0.85 | W exceeds 33 ms
Saturated | ρ ≥ 1.00 | W capped at 2 s
M/M/1 delay characteristic:
W
ρ
0.6
0.85
W = L_min/(1-ρ) → ∞ as ρ → 1
Low ρ: W ≈ L_min = 5 ms
Steep divergence
after ρ = 0.85

## Slide 11
NETWORK LAYER
Communication Architecture & Messages
UAM Corridor Simulation · Toyota/TEMA 2026
Communication graph G = (V, E)
V: UAM nodes · BS nodes · one GCS node
E: directed (UAM → BS), (BS → UAM) per connected vehicle; (BS → GCS) always present
Edge attributes: quality ∈ {good, degraded}, rtt [s], rtt_ok [bool]
Messages per UAM per step
Message class | Size / Rate | Bit rate | Purpose
Basic Safety Msg (BSM) | 300 B × 10 Hz | 24 kbps | Position, velocity, identity — all nodes
HOTL control stream | Supervisory telemetry | 35 kbps | Aircraft health; human monitors only
HWTL video stream | Live video + commands | 6 Mbps | Full HD feed; human pilots actively
R_i = R_BSM + R_ctrl = { 59 kbps (HOTL) | 6,024 kbps ≈ 6 Mbps (HWTL) }
Per-step message count (for buffer tracking): 10 BSM + 10 control = 20 msgs/UAM/step (at Δt = 1 s)
BSM: conceptually aligned with ASTM F3548 / GUTMA UTM message formats

## Slide 12
NETWORK LAYER
Round-Trip Time (RTT)
UAM Corridor Simulation · Toyota/TEMA 2026
RTT_i = 2 × ( t_prop + W_j + t_bh ) + δ_HO
Component | Formula / Value | Note
Propagation delay | t_prop = d_ij / c, c = 3×10⁸ m/s | d ≈ 300–3,000 m → t_prop ≈ 1–10 µs (tiny)
Queuing delay | W_j = L_min / (1-ρ_j) | M/M/1; dominates RTT at high load
Backhaul delay | t_bh = 10 ms (fixed) | BS–GCS link latency
Handoff penalty | δ_HO = 100 ms (if in_handoff) | Added once during active handoff
Normal
ρ ≪ 1
RTT ≈ 21 ms
2 × (0 + 5 ms + 10 ms)
Stressed
ρ = 0.85
RTT ≈ 87 ms
2 × (0 + 33 ms + 10 ms)
Saturated
ρ ≥ 1
RTT ≈ 4 s
2 × (0 + 2 s + 10 ms)
RTT_max = 500 ms

## Slide 13
NETWORK LAYER
Handoff Algorithm
UAM Corridor Simulation · Toyota/TEMA 2026
1
Coverage scan
Compute d_ij to all BS.
Candidate set C_i = { j : d_ij ≤ r_deg }
2
Best BS selection
Sort C_i by distance.
Nearest BS = candidate j*
3
Hysteresis check
Trigger handoff only if
d_ij* ≤ 0.8 × d_i,prev
(must be 20% closer)
4
Execution
Remove old edges from G.
in_handoff = true for T_HO = 200 ms.
Drop each msg with p_drop = 0.1
5
Graph update
Add edges (u_i, j*) and (j*, u_i)
with quality {good|degraded}
T_HO = 200 ms · p_drop = 0.10 · δ_HO = +100 ms · hysteresis = 20% closer required

## Slide 14
KPI DEFINITIONS
Safety & Performance Metrics
UAM Corridor Simulation · Toyota/TEMA 2026
KPI | Formula / Computation | Threshold / Alert
Min separation time | T_sep = Δx / v_follower (pairwise) | Violation if T_sep < 2 s
Max RTT | RTT_i = 2(t_prop + W_j + t_bh) + δ_HO | Violation if RTT > 500 ms
Drop rate | (msgs_dropped) / (dropped + processed) | Alert if > 5%
BS load factor | ρ_j = λ_arr / C_j | Warn ≥ 60% ¦ Critical ≥ 85%
No-coverage count | UAMs with serving_bs = None, per step | Any count > 0 is concerning
Handoff count | UAMs in active handoff, per step | Trend indicator
Concurrent HWTL | Sum of UAMs in HWTL mode, per step | Directly drives BS load
Separation violations | Cumulative steps with T_sep < τ_viol | Zero tolerance
Scenario classification: NORMAL if ρ_max < 0.85 & drop rate < 5% & no sep violations. DEGRADED if drop rate ≥ 5% or any BS time-in-red > 10%. UNSAFE if separation violated.

## Slide 15
KPI DEFINITIONS
KPI Dependency Chain
UAM Corridor Simulation · Toyota/TEMA 2026
UAM count
+ mode mix
→
BS traffic
load ρ
→
M/M/1
delay W
→
RTT per
UAM
→
Safety
classification
Key non-linearity: one HWTL aircraft = ~100 HOTL aircraft in bandwidth demand
E[concurrent HWTL] = N_UAM × λ_hr/3600 × d̅
At baseline (N=50, λ=0.5/hr, d̄=60 s): E[HWTL] ≈ 0.42 → ρ ≈ 3.7% → safe
At cascade (N=60, λ=8/hr, d̄=90 s): E[HWTL] ≈ 12 → ρ ≈ 63% → yellow; with surge → saturated

## Slide 16
SCENARIOS
Four Prototype Experiments
UAM Corridor Simulation · Toyota/TEMA 2026
# | Scenario | N | M BS | C [Mbps] | λ_hr | External Load | Result
1 | Baseline | 50 | 16 | 100 | 0.5 | None | NORMAL
2 | High Density | 150 | 16 | 50 | 0.5 | None | UNSAFE
3 | Frequent Switches | 80 | 16 | 100 | 5.0 | None | NORMAL
4 | Cascade Failure | 60 | 6 | 20 | 8.0 | +8 Mbps t=120-360 s | UNSAFE
Design principle: scenarios stress one variable at a time — traffic density, switch rate, or infrastructure fragility.
S1 Baseline:
Infrastructure sized with ample headroom → ρ ≈ 3%, RTT ≈ 21 ms
S2 High Density:
3× UAMs + halved capacity → BS near destination saturates; separation violations emerge
S3 Freq. Switches:
10× switch rate manageable when N is modest — towers were sized for video bursts
S4 Cascade Failure:
Dual trigger (HWTL accumulation + terrestrial surge) tips already-stressed BS to ρ > 100%

## Slide 17
SCENARIOS · S1
Scenario 1: Baseline
UAM Corridor Simulation · Toyota/TEMA 2026
Parameters
UAMs:
50
BS:
16 × 100 Mbps
Spacing:
4,706 m
λ_hr:
0.5 / UAM / hr
d̄_HWTL:
60 s
External:
None
Key Outcomes
Avg RTT:
~21 ms
BS load ρ:
~3–4%
Drop rate:
<0.1%
Sep viol.:
0
Concurrent HWTL:
~0.4
VERDICT
NORMAL
Plain-English Interpretation
A normal business day on a future air corridor. 50 aircraft are spaced out evenly, flying comfortably. Cell towers handle the trickle of telemetry traffic with plenty of bandwidth to spare — no queues building, no RTT spikes. This is what the system was designed to look like under nominal operating conditions.

## Slide 18
SCENARIOS · S2
Scenario 2: High Density
UAM Corridor Simulation · Toyota/TEMA 2026
Parameters
UAMs:
150 (3×)
BS:
16 × 50 Mbps
Lanes:
2
λ_hr:
0.5 / UAM / hr
τ_min:
3 s
External:
None
Key Outcomes
Peak BS load:
>100%
Max RTT:
> 500 ms
Drop rate:
> 5%
Sep viol.:
Many
Classification:
UNSAFE
VERDICT
UNSAFE
Plain-English Interpretation
Rush hour in the sky. With 3× the usual aircraft sharing the same route and halved BS capacity, two compounding problems emerge: aircraft bunch near the San Jose hub, flooding one BS; and the shrinking gap ahead of each aircraft breaches the minimum headway. Infrastructure overload and airspace safety degrade simultaneously — not because one thing broke, but because more vehicles were packed into a space designed for fewer.

## Slide 19
SCENARIOS · S3
Scenario 3: Frequent Switches (λ = 5/hr)
UAM Corridor Simulation · Toyota/TEMA 2026
Parameters
UAMs:
80
BS:
16 × 100 Mbps
λ_hr:
5.0 / UAM / hr
d̄_HWTL:
45 s
Switch:
10× baseline rate
External:
None
Key Outcomes
Avg RTT:
~25 ms
Peak BS load:
~18–22%
Drop rate:
<0.5%
Sep viol.:
0
Classification:
NORMAL
VERDICT
NORMAL
Plain-English Interpretation
Pilots take manual control 10× more often than baseline — each intervention triggers a 6 Mbps video stream. Like switching from SMS to video-call. Despite the extra load, the corridor handles it: with 80 aircraft (not 150), and towers sized with headroom for video bursts, utilization stays below 25%. The system demonstrates that occasional human intervention is not inherently dangerous — it just needs infrastructure sized to absorb it.

## Slide 20
SCENARIOS · S4
Scenario 4: Cascade Failure
UAM Corridor Simulation · Toyota/TEMA 2026
Parameters
UAMs:
60
BS:
6 × 20 Mbps
λ_hr:
8.0 / UAM / hr
d̄_HWTL:
90 s
Surge:
+8 Mbps @ t=120–360 s
E[HWTL/BS]:
≈ 2 at steady state
Key Outcomes
Phase 1 ρ:
~3% (green)
Phase 2 ρ:
~63% (yellow)
Phase 3 ρ:
>100% (red)
Max RTT:
2,000+ ms
Classification:
UNSAFE
VERDICT
UNSAFE
Plain-English Interpretation
Two ordinary events at the wrong time. HWTL episodes accumulate, stressing the 6-BS, 20 Mbps network to 63% utilization. Then a stadium empties: tens of thousands of phones start streaming, sharing the exact same cell towers as the aircraft. The +8 Mbps terrestrial surge tips already-stressed BSs past ρ = 1. RTT balloons from milliseconds to seconds. Commands stop arriving in time. The towers failed because two unrelated groups needed the same resource simultaneously — and no one planned for the collision.

## Slide 21
VALIDATION & ROADMAP
Known Limitations & Planned Sub-Model Replacements
UAM Corridor Simulation · Toyota/TEMA 2026
Component | Current Model (Prototype) | Planned Replacement
UAV kinematics | Instantaneous speed adjustment; no inertia | IDM or eVTOL thrust/drag model calibrated to Joby S4 / Toyota NX specs
Separation standard | τ_min = 2–5 s (AI placeholder) | FAA/EASA UAM separation minima or operator-specific envelope
Radio propagation | Binary distance threshold (no path loss) | A2G path-loss model (free-space + terrain/building shielding)
Link capacity | Fixed BS throughput ceiling | SINR-based spectral efficiency; frequency reuse across adjacent cells
5G queuing | M/M/1 single-class | M/M/1/K (finite buffer) or M/D/1; multi-priority for UAM vs ground users
Corridor geometry | 1D linear, uniform BS placement | SF–SJ geographic waypoints; no-fly zones; multi-lane 3D corridors
Network topology | Static ground BS only | HAPS / LEO relay nodes; moving-relay topology
HWTL trigger model | Stationary Poisson process | Event-driven: weather, airspace conflict, ATC instruction, payload
The prototype is architecturally correct — the coupling mechanism is faithfully modeled. Validation requires substituting real-world sub-models and calibrating to Joby / Toyota performance data.

## Slide 22
VALIDATION & ROADMAP
Development Roadmap
UAM Corridor Simulation · Toyota/TEMA 2026
Phase 1
(Now)
1D Corridor Prototype
· AI-default parameters
· 4 scenario experiments
· Coupled queuing + traffic model
· HTML/PPTX reports
→
Phase 2
Validated Sub-Models
· Joby S4 & Toyota NX specs
· A2G path-loss model
· SINR-based link capacity
· Event-triggered HWTL
→
Phase 3
SF–SJ Geography
· Geographic waypoints
· No-fly zones
· Terrain shielding
· Multi-lane 3D corridors
→
Phase 4
Network-Level Effects
· Multi-corridor topology
· HAPS / moving relay
· Multi-priority 5G queuing
· Regulatory scenario analysis
Data needs from Toyota / Joby: aircraft performance envelope, actual BSM message specs, network QoS requirements, operational HWTL frequency statistics.

## Slide 23
APPENDIX
Key Equations Summary
UAM Corridor Simulation · Toyota/TEMA 2026
3D UAM–BS distance
d_ij = sqrt[ (x_jᴵˢ - x_i)² + (y_jᴵˢ)² + h² ]
BS traffic intensity
ρ_j = Σ_{i ∈ S_j} R_i / C_j
M/M/1 queuing delay
W_j = L_min / (1 - ρ_j), ρ_j < 1 (ρ_j ≥ 1: cap at 2 s)
Round-trip time
RTT_i = 2(d_ij/c + W_j + t_bh) + δ_HO
Separation time
T_sep,i = (x_{i+1} - x_i) / v_i
Car-following speed adjust
v_i* = max( Δx / τ_min, 0 )
Mode-switch inter-arrival
T_switch ~ Exp(λ_hr / 3600)
HWTL episode duration
D_HWTL ~ Exp(1 / d̅)
Expected concurrent HWTL
E[HWTL] = N × λ_hr/3600 × d̅

## Slide 24
APPENDIX
Complete Default Parameter Table
UAM Corridor Simulation · Toyota/TEMA 2026
Parameter | Symbol | Default Value
Simulation horizon | T | 600 s
Time step | Δt | 1.0 s
Corridor length | L | 80,000 m
Corridor altitude | h | 300 m AGL
UAM speed range | [v_min, v_max] | [40, 60] m/s
Min separation time | τ_min | 5.0 s
Violation threshold | τ_viol | 2.0 s
BS spacing (baseline) | Δx | ≈4,706 m
BS capacity (baseline) | C | 100 Mbps
Good-coverage radius | r_good | 3,000 m
Degraded-coverage radius | r_deg | 6,000 m
Buffer capacity | B | 500 msgs
BSM size | — | 300 bytes
BSM rate | — | 10 Hz
HOTL control rate | R_HOTL | 35 kbps
HWTL video rate | R_HWTL | 6 Mbps
RTT safety threshold | RTT_max | 500 ms
Base processing delay | L_min | 5 ms
Backhaul delay | t_bh | 10 ms
Handoff duration | T_HO | 200 ms
Drop prob. (handoff) | p_drop | 0.10
Default switch rate | λ_hr | 0.5 / UAM / hr
Default HWTL duration | d̅ | 60 s
Load warning threshold | — | 60%
Load critical threshold | — | 85%